## Slide 1: Chương 13: Hệ thống tập tin
NHẬP MÔN HỆ ĐIỀU HÀNH
502047

## Slide 2: Ghi chú về bản quyền
Toàn bộ nội dung slide này tải về từ https://www.os-book.com/OS10/slide-dir/index.html , sinh viên có quyền tải về, lưu trữ, in ấn, tham khảo cho mục đích học tập. Sinh viên không được phát hành lại hay thay đổi nội dung slide nếu chưa có sự đồng ý của tác giả.
Phần ghi chú ở cuối slide (nếu có) là do các thầy cô ghi chú lại trong quá trình giảng dạy.

## Slide 3: Outline
File Concept
Access Methods
Disk and Directory Structure
File-System Mounting
File Sharing
Protection

## Slide 4: Objectives
To explain the function of file systems
To describe the interfaces to file systems
To discuss file-system design tradeoffs, including access methods, file sharing, file locking, and directory structures
To explore file-system protection

## Slide 5: File Concept
Contiguous logical address space
Types:
  Data
    numeric
    character
    binary
  Program
Contents defined by file’s creator
  Many types
    Consider text file, source file, executable file

## Slide 6: File Attributes
Name – only information kept in human-readable form
Identifier – unique tag (number) identifies file within file system
Type – needed for systems that support different types
Location – pointer to file location on device
Size – current file size
Protection – controls who can do reading, writing, executing
Time, date, and user identification – data for protection, security, and usage monitoring
Information about files are kept in the directory structure, which is maintained on the disk
Many variations, including extended file attributes such as file checksum
Information kept in the directory structure

## Slide 7: File info Window on Mac OS X

## Slide 8: File Operations
File is an abstract data type
Create
Write – at write pointer location
Read – at read pointer location
Reposition within file - seek
Delete
Truncate
Open(Fi) – search the directory structure on disk for entry Fi, and move the content of entry to memory
Close (Fi) – move the content of entry Fi in memory to directory structure on disk

## Slide 9: Open Files
Several pieces of data are needed to manage open files:
  Open-file table: tracks open files
  File pointer: pointer to last read/write location, per process that has the file open
  File-open count: counter of number of times a file is open – to allow removal of data from open-file table when last processes closes it
  Disk location of the file: cache of data access information
  Access rights: per-process access mode information

## Slide 10: Open File Locking
Provided by some operating systems and file systems
  Similar to reader-writer locks
  Shared lock similar to reader lock – several processes can acquire concurrently
  Exclusive lock similar to writer lock
Mediates access to a file
Mandatory or advisory:
  Mandatory – access is denied depending on locks held and requested
  Advisory – processes can find status of locks and decide what to do

## Slide 11: File Locking Example – Java API
import java.io.*;
import java.nio.channels.*;
public class LockingExample {
public static final boolean EXCLUSIVE = false;
public static final boolean SHARED = true;
public static void main(String arsg[]) throws IOException {
FileLock sharedLock = null;
FileLock exclusiveLock = null;
try {
RandomAccessFile raf = new RandomAccessFile("file.txt", "rw");
// get the channel for the file
FileChannel ch = raf.getChannel();
// this locks the first half of the file - exclusive
exclusiveLock = ch.lock(0, raf.length()/2, EXCLUSIVE);
/** Now modify the data . . . */
// release the lock
exclusiveLock.release();

## Slide 12: File Locking Example – Java API (Cont.)
// this locks the second half of the file - shared
sharedLock = ch.lock(raf.length()/2+1, raf.length(), SHARED);
/** Now read the data . . . */
// release the lock
sharedLock.release();
} catch (java.io.IOException ioe) {
System.err.println(ioe);
}finally {
if (exclusiveLock != null)
exclusiveLock.release();
if (sharedLock != null)
sharedLock.release();
}
}
}

## Slide 13: File Types – Name, Extension

## Slide 14: File Structure
None - sequence of words, bytes
Simple record structure
  Lines
  Fixed length
  Variable length
Complex Structures
  Formatted document
  Relocatable load file
Can simulate last two with first method by inserting appropriate control characters
Who decides:
  Operating system
  Program

## Slide 15: Sequential-access File

## Slide 16: Access Methods
Sequential Access
read next
write next
reset
no read after last write
(rewrite)
Direct Access – file is fixed length logical records
read n
write n
position to n
read next
write next
rewrite n
n = relative block number
Relative block numbers allow OS to decide where file should be placed
  See allocation problem in Ch 12

## Slide 17: Simulation of Sequential Access on Direct-access File

## Slide 18: Other Access Methods
Can be built on top of base methods
General involve creation of an index for the file
Keep index in memory for fast determination of location of data to be operated on (consider UPC code plus record of data about that item)
If too large, index (in memory) of the index (on disk)
IBM indexed sequential-access method (ISAM)
  Small master index, points to disk blocks of secondary index
  File kept sorted on a defined key
  All done by the OS
VMS operating system provides index and relative files as another example (see next slide)

## Slide 19: Example of Index and Relative Files

## Slide 20: Directory Structure
A collection of nodes containing information about all files
F 1
F 2
F 3
F 4
F n
Directory
Files
Both the directory structure and the files reside on disk

## Slide 21: Disk Structure
Disk can be subdivided into partitions
Disks or partitions can be RAID protected against failure
Disk or partition can be used raw – without a file system, or formatted with a file system
Partitions also known as minidisks, slices
Entity containing file system known as a volume
Each volume containing file system also tracks that file system’s info in device directory or volume table of contents
As well as general-purpose file systems there are many special-purpose file systems, frequently all within the same operating system or computer

## Slide 22: A Typical File-system Organization

## Slide 23: Types of File Systems
We mostly talk of general-purpose file systems
But systems frequently have may file systems, some general- and some special- purpose
Consider Solaris has
  tmpfs – memory-based volatile FS for fast, temporary I/O
  objfs – interface into kernel memory to get kernel symbols for debugging
  ctfs – contract file system for managing daemons
  lofs – loopback file system allows one FS to be accessed in place of another
  procfs – kernel interface to process structures
  ufs, zfs – general purpose file systems

## Slide 24: Operations Performed on Directory
Search for a file
Create a file
Delete a file
List a directory
Rename a file
Traverse the file system

## Slide 25: Directory Organization
Efficiency – locating a file quickly
Naming – convenient to users
  Two users can have same name for different files
  The same file can have several different names
Grouping – logical grouping of files by properties, (e.g., all Java programs, all games, …)
The directory is organized logically to obtain

## Slide 26: Single-Level Directory
A single directory for all users
Naming problem
Grouping problem

## Slide 27: Two-Level Directory
Separate directory for each user
Path name
Can have the same file name for different user
Efficient searching
No grouping capability

## Slide 28: Tree-Structured Directories

## Slide 29: Tree-Structured Directories (Cont.)
Efficient searching
Grouping Capability
Current directory (working directory)
  cd /spell/mail/prog
  type list

## Slide 30: Tree-Structured Directories (Cont.)
Absolute or relative path name
Creating a new file is done in current directory
Delete a file
rm <file-name>
Creating a new subdirectory is done in current directory
  mkdir <dir-name>
  Example: if in current directory /mail
  mkdir count
Deleting “mail”  deleting the entire subtree rooted by “mail”

## Slide 31: Acyclic-Graph Directories
Have shared subdirectories and files

## Slide 32: Acyclic-Graph Directories (Cont.)
Two different names (aliasing)
If dict deletes list  dangling pointer
Solutions:
  Backpointers, so we can delete all pointers Variable size records a problem
  Backpointers using a daisy chain organization
  Entry-hold-count solution
New directory entry type
  Link – another name (pointer) to an existing file
  Resolve the link – follow pointer to locate the file

## Slide 33: General Graph Directory

## Slide 34: General Graph Directory (Cont.)
How do we guarantee no cycles?
  Allow only links to file not subdirectories
  Garbage collection
  Every time a new link is added use a cycle detection algorithm to determine whether it is OK

## Slide 35: File System Mounting
A file system must be mounted before it can be accessed
A unmounted file system (i.e., Fig. 11-11(b)) is mounted at a mount point

## Slide 36: Mount Point

## Slide 37: File Sharing
Sharing of files on multi-user systems is desirable
Sharing may be done through a protection scheme
On distributed systems, files may be shared across a network
Network File System (NFS) is a common distributed file-sharing method
If multi-user system
  User IDs identify users, allowing permissions and protections to be per-user Group IDs allow users to be in groups, permitting group access rights
  Owner of a file / directory
  Group of a file / directory

## Slide 38: File Sharing – Remote File Systems
Uses networking to allow file system access between systems
  Manually via programs like FTP
  Automatically, seamlessly using distributed file systems
  Semi automatically via the world wide web
Client-server model allows clients to mount remote file systems from servers
  Server can serve multiple clients
  Client and user-on-client identification is insecure or complicated
  NFS is standard UNIX client-server file sharing protocol
  CIFS is standard Windows protocol
  Standard operating system file calls are translated into remote calls
Distributed Information Systems (distributed naming services) such as LDAP, DNS, NIS, Active Directory implement unified access to information needed for remote computing

## Slide 39: File Sharing – Failure Modes
All file systems have failure modes
  For example corruption of directory structures or other non-user data, called metadata
Remote file systems add new failure modes, due to network failure, server failure
Recovery from failure can involve state information about status of each remote request
Stateless protocols such as NFS v3 include all information in each request, allowing easy recovery but less security

## Slide 40: File Sharing – Consistency Semantics
Specify how multiple users are to access a shared file simultaneously
  Similar to Ch 5 process synchronization algorithms
    Tend to be less complex due to disk I/O and network latency (for remote file systems
  Andrew File System (AFS) implemented complex remote file sharing semantics
  Unix file system (UFS) implements:
    Writes to an open file visible immediately to other users of the same open file
    Sharing file pointer to allow multiple users to read and write concurrently
  AFS has session semantics
    Writes only visible to sessions starting after the file is closed

## Slide 41: Protection
File owner/creator should be able to control:
  what can be done
  by whom
Types of access
  Read
  Write
  Execute
  Append
  Delete
  List

## Slide 42: Access Lists and Groups
Mode of access: read, write, execute
Three classes of users on Unix / Linux
RWX
a) owner access 7  1 1 1 RWX
b) group access 6  1 1 0
RWX
c) public access 1  0 0 1
Ask manager to create a group (unique name), say G, and add some users to the group.
For a particular file (say game) or subdirectory, define an appropriate access.
Attach a group to a file chgrp G game

## Slide 43: Windows 7 Access-Control List Management

## Slide 44: A Sample UNIX Directory Listing

## Slide 45: End of Chapter 13

## Slide 46: Chapter 14: File System Implementation

## Slide 47: Outline
File-System Structure
File-System Operations
Directory Implementation
Allocation Methods
Free-Space Management
Efficiency and Performance
Recovery
Example: WAFL File System

## Slide 48: Objectives
Describe the details of implementing local file systems and directory structures
Discuss block allocation and free-block algorithms and trade-offs
Explore file system efficiency and performance issues
Look at recovery from file system failures
Describe the WAFL file system as a concrete example

## Slide 49: File-System Structure
File structure
  Logical storage unit
  Collection of related information
File system resides on secondary storage (disks)
  Provided user interface to storage, mapping logical to physical
  Provides efficient and convenient access to disk by allowing data to be stored, located retrieved easily
Disk provides in-place rewrite and random access
  I/O transfers performed in blocks of sectors (usually 512 bytes)
File control block (FCB) – storage structure consisting of information about a file
Device driver controls the physical device
File system organized into layers

## Slide 50: Layered File System

## Slide 51: File System Layers
Device drivers manage I/O devices at the I/O control layer
  Given commands like “read drive1, cylinder 72, track 2, sector 10, into memory location 1060” outputs low-level hardware specific commands to hardware controller
Basic file system given command like “retrieve block 123” translates to device driver
Also manages memory buffers and caches (allocation, freeing, replacement)
  Buffers hold data in transit
  Caches hold frequently used data
File organization module understands files, logical address, and physical blocks
  Translates logical block # to physical block #
  Manages free space, disk allocation

## Slide 52: File System Layers (Cont.)
Logical file system manages metadata information
  Translates file name into file number, file handle, location by maintaining file control blocks (inodes in UNIX)
  Directory management
  Protection
Layering useful for reducing complexity and redundancy, but adds overhead and can decrease performance
Logical layers can be implemented by any coding method according to OS designer

## Slide 53: File System Layers (Cont.)
Many file systems, sometimes many within an operating system
  Each with its own format (CD-ROM is ISO 9660; Unix has UFS, FFS; Windows has FAT, FAT32, NTFS as well as floppy, CD, DVD Blu-ray, Linux has more than 130 types, with extended file system ext3 and ext4 leading; plus distributed file systems, etc.)
  New ones still arriving – ZFS, GoogleFS, Oracle ASM, FUSE

## Slide 54: File-System Operations
We have system calls at the API level, but how do we implement their functions?
  On-disk and in-memory structures
Boot control block contains info needed by system to boot OS from that volume
  Needed if volume contains OS, usually first block of volume
Volume control block (superblock, master file table) contains volume details
  Total # of blocks, # of free blocks, block size, free block pointers or array
Directory structure organizes the files
  Names and inode numbers, master file table

## Slide 55: File-System Implementation (Cont.)
Per-file File Control Block (FCB) contains many details about the file
  typically inode number, permissions, size, dates
  NFTS stores into in master file table using relational DB structures

## Slide 56: In-Memory File System Structures
Mount table storing file system mounts, mount points, file system types
system-wide open-file table contains a copy of the FCB of each file and other info
per-process open-file table contains pointers to appropriate entries in system-wide open-file table as well as other info
The following figure illustrates the necessary file system structures provided by the operating systems
Figure 12-3(a) refers to opening a file
Figure 12-3(b) refers to reading a file
Plus buffers hold data blocks from secondary storage
Open returns a file handle for subsequent use
Data from read eventually copied to specified user process memory address

## Slide 57: In-Memory File System Structures

## Slide 58: Directory Implementation
Linear list of file names with pointer to the data blocks
  Simple to program
  Time-consuming to execute
    Linear search time
    Could keep ordered alphabetically via linked list or use B+ tree
Hash Table – linear list with hash data structure
  Decreases directory search time
  Collisions – situations where two file names hash to the same location
  Only good if entries are fixed size, or use chained-overflow method

## Slide 59: Allocation Methods - Contiguous
An allocation method refers to how disk blocks are allocated for files:
Contiguous allocation – each file occupies set of contiguous blocks
  Best performance in most cases
  Simple – only starting location (block #) and length (number of blocks) are required
  Problems include finding space for file, knowing file size, external fragmentation, need for compaction off-line (downtime) or on-line

## Slide 60: Contiguous Allocation
Mapping from logical to physical
LA/512
Q
R
  Block to be accessed = Q + starting address
  Displacement into block = R

## Slide 61: Extent-Based Systems
Many newer file systems (i.e., Veritas File System) use a modified contiguous allocation scheme
Extent-based file systems allocate disk blocks in extents
An extent is a contiguous block of disks
  Extents are allocated for file allocation
  A file consists of one or more extents

## Slide 62: Allocation Methods - Linked
Linked allocation – each file a linked list of blocks
  File ends at nil pointer
  No external fragmentation
  Each block contains pointer to next block
  No compaction, external fragmentation
  Free space management system called when new block needed
  Improve efficiency by clustering blocks into groups but increases internal fragmentation
  Reliability can be a problem
  Locating a block can take many I/Os and disk seeks

## Slide 63: Allocation Methods – Linked (Cont.)
FAT (File Allocation Table) variation
  Beginning of volume has table, indexed by block number
  Much like a linked list, but faster on disk and cacheable
  New block allocation simple

## Slide 64: Linked Allocation
Each file is a linked list of disk blocks: blocks may be scattered anywhere on the disk
pointer
block =
Mapping
  Block to be accessed is the Qth block in the linked chain of blocks representing the file.
  Displacement into block = R + 1
LA/511
Q
R

## Slide 65: Linked Allocation

## Slide 66: File-Allocation Table

## Slide 67: Allocation Methods - Indexed
Indexed allocation
  Each file has its own index block(s) of pointers to its data blocks
Logical view

## Slide 68: Example of Indexed Allocation

## Slide 69: Indexed Allocation (Cont.)
Need index table
Random access
Dynamic access without external fragmentation, but have overhead of index block
Mapping from logical to physical in a file of maximum size of 256K bytes and block size of 512 bytes. We need only 1 block for index table
LA/512
Q
R
Q = displacement into index table
R = displacement into block

## Slide 70: Indexed Allocation – Mapping (Cont.)
Mapping from logical to physical in a file of unbounded length (block size of 512 words)
Linked scheme – Link blocks of index table (no limit on size)
LA / (512 x 511)
Q1
R1
  Q1 = block of index table
  R1 is used as follows:
R1 / 512
Q2
R2
  Q2 = displacement into block of index table
  R2 displacement into block of file:

## Slide 71: Indexed Allocation – Mapping (Cont.)
Two-level index (4K blocks could store 1,024 four-byte pointers in outer index -> 1,048,567 data blocks and file size of up to 4GB)
LA / (512 x 512)
Q1
R1
  Q1 = displacement into outer-index
  R1 is used as follows:
R1 / 512
Q2
R2
  Q2 = displacement into block of index table
  R2 displacement into block of file:

## Slide 72: Indexed Allocation – Mapping (Cont.)

## Slide 73: Combined Scheme: UNIX UFS
More index blocks than can be addressed with 32-bit file pointer
4K bytes per block, 32-bit addresses

## Slide 74: Performance
Best method depends on file access type
  Contiguous great for sequential and random
Linked good for sequential, not random
Declare access type at creation -> select either contiguous or linked
Indexed more complex
  Single block access could require 2 index block reads then data block read
  Clustering can help improve throughput, reduce CPU overhead
For NVM, no disk head so different algorithms and optimizations needed
  Using old algorithm uses many CPU cycles trying to avoid non-existent head movement
  With NVM goal is to reduce CPU cycles and overall path needed for I/O

## Slide 75: Performance (Cont.)
Adding instructions to the execution path to save one disk I/O is reasonable
  Intel Core i7 Extreme Edition 990x (2011) at 3.46Ghz = 159,000 MIPS
    http://en.wikipedia.org/wiki/Instructions_per_second
  Typical disk drive at 250 I/Os per second
    159,000 MIPS / 250 = 630 million instructions during one disk I/O
  Fast SSD drives provide 60,000 IOPS
    159,000 MIPS / 60,000 = 2.65 millions instructions during one disk I/O

## Slide 76: Free-Space Management
File system maintains free-space list to track available blocks/clusters
  (Using term “block” for simplicity)
Bit vector or bit map (n blocks)
…
0
1
2
n-1
bit[i] =

1  block[i] free
0  block[i] occupied
Block number calculation
(number of bits per word) *
(number of 0-value words) +
offset of first 1 bit
CPUs have instructions to return offset within word of first “1” bit

## Slide 77: Free-Space Management (Cont.)
Bit map requires extra space
  Example:
block size = 4KB = 212 bytes
disk size = 240 bytes (1 terabyte)
n = 240/212 = 228 bits (or 32MB)
if clusters of 4 blocks -> 8MB of memory
Easy to get contiguous files

## Slide 78: Linked Free Space List on Disk
Linked list (free list)
  Cannot get contiguous space easily
  No waste of space
  No need to traverse the entire list (if # free blocks recorded)

## Slide 79: Free-Space Management (Cont.)
Grouping
  Modify linked list to store address of next n-1 free blocks in first free block, plus a pointer to next block that contains free-block-pointers (like this one)
Counting
  Because space is frequently contiguously used and freed, with contiguous-allocation allocation, extents, or clustering
    Keep address of first free block and count of following free blocks
    Free space list then has entries containing addresses and counts

## Slide 80: Free-Space Management (Cont.)
Space Maps
  Used in ZFS
  Consider meta-data I/O on very large file systems
    Full data structures like bit maps couldn’t fit in memory -> thousands of I/Os
  Divides device space into metaslab units and manages metaslabs
    Given volume can contain hundreds of metaslabs
  Each metaslab has associated space map
    Uses counting algorithm
  But records to log file rather than file system
    Log of all block activity, in time order, in counting format
  Metaslab activity -> load space map into memory in balanced-tree structure, indexed by offset
    Replay log into that structure
    Combine contiguous free blocks into single entry

## Slide 81: TRIMing Unused Blocks
HDDS overwrite in place so need only free list
Blocks not treated specially when freed
  Keeps its data but without any file pointers to it, until overwritten
Storage devices not allowing overwrite (like NVM) suffer badly with same algorithm
  Must be erased before written, erases made in large chunks (blocks, composed of pages) and are slow
  TRIM is a newer mechanism for the file system to inform the NVM storage device that a page is free
    Can be garbage collected or if block is free, now block can be erased

## Slide 82: Efficiency and Performance
Efficiency dependent on:
  Disk allocation and directory algorithms
  Types of data kept in file’s directory entry
  Pre-allocation or as-needed allocation of metadata structures
  Fixed-size or varying-size data structures

## Slide 83: Efficiency and Performance (Cont.)
Performance
  Keeping data and metadata close together
  Buffer cache – separate section of main memory for frequently used blocks
  Synchronous writes sometimes requested by apps or needed by OS
    No buffering / caching – writes must hit disk before acknowledgement
    Asynchronous writes more common, buffer-able, faster
  Free-behind and read-ahead – techniques to optimize sequential access
  Reads frequently slower than writes

## Slide 84: Page Cache
A page cache caches pages rather than disk blocks using virtual memory techniques and addresses
Memory-mapped I/O uses a page cache
Routine I/O through the file system uses the buffer (disk) cache
This leads to the following figure

## Slide 85: I/O Without a Unified Buffer Cache

## Slide 86: Unified Buffer Cache
A unified buffer cache uses the same page cache to cache both memory-mapped pages and ordinary file system I/O to avoid double caching
  But which caches get priority, and what replacement algorithms to use?

## Slide 87: I/O Using a Unified Buffer Cache

## Slide 88: Recovery
Consistency checking – compares data in directory structure with data blocks on disk, and tries to fix inconsistencies
  Can be slow and sometimes fails
Use system programs to back up data from disk to another storage device (magnetic tape, other magnetic disk, optical)
Recover lost file or disk by restoring data from backup

## Slide 89: Log Structured File Systems
Log structured (or journaling) file systems record each metadata update to the file system as a transaction
All transactions are written to a log
  A transaction is considered committed once it is written to the log (sequentially)
  Sometimes to a separate device or section of disk
  However, the file system may not yet be updated
The transactions in the log are asynchronously written to the file system structures
  When the file system structures are modified, the transaction is removed from the log
If the file system crashes, all remaining transactions in the log must still be performed
Faster recovery from crash, removes chance of inconsistency of metadata

## Slide 90: Example: WAFL File System
Used on Network Appliance “Filers” – distributed file system appliances
“Write-anywhere file layout”
Serves up NFS, CIFS, http, ftp
Random I/O optimized, write optimized
  NVRAM for write caching
Similar to Berkeley Fast File System, with extensive modifications

## Slide 91: The WAFL File Layout

## Slide 92: Snapshots in WAFL

## Slide 93: The Apple File System

## Slide 94: End of Chapter 14

## Slide 95: Chapter 15: File System Internals

## Slide 96: Outline
File Systems
File-System Mounting
Partitions and Mounting
File Sharing
Virtual File Systems
Remote File Systems
Consistency Semantics
NFS

## Slide 97: Objectives
Delve into the details of file systems and their implementation
Explore booting and file sharing
Describe remote file systems, using NFS as an example

## Slide 98: File System
General-purpose computers can have multiple storage devices
  Devices can be sliced into partitions, which hold volumes
  Volumes can span multiple partitions
  Each volume usually formatted into a file system
  # of file systems varies, typically dozens available to choose from Typical storage device organization:

## Slide 99: Example Mount Points and File Systems - Solaris

## Slide 100: Partitions and Mounting
Partition can be a volume containing a file system (“cooked”) or raw – just a sequence of blocks with no file system
Boot block can point to boot volume or boot loader set of blocks that contain enough code to know how to load the kernel from the file system
  Or a boot management program for multi-os booting
Root partition contains the OS, other partitions can hold other OSes, other file systems, or be raw
  Mounted at boot time
  Other partitions can mount automatically or manually on mount points – location at which they can be accessed
At mount time, file system consistency checked
  Is all metadata correct?
    If not, fix it, try again
    If yes, add to mount table, allow access

## Slide 101: File Systems and Mounting
Unix-like file system directory tree
Unmounted file system
After mounting (b) into the existing directory tree

## Slide 102: File Sharing
Allows multiple users / systems access to the same files
Permissions / protection must be implement and accurate
  Most systems provide concepts of owner, group member
  Must have a way to apply these between systems

## Slide 103: Virtual File Systems
Virtual File Systems (VFS) on Unix provide an object-oriented way of implementing file systems
VFS allows the same system call interface (the API) to be used for different types of file systems
  Separates file-system generic operations from implementation details
  Implementation can be one of many file systems types, or network file system
    Implements vnodes which hold inodes or network file details
  Then dispatches operation to appropriate file system implementation routines

## Slide 104: Virtual File Systems (Cont.)
The API is to the VFS interface, rather than any specific type of file system

## Slide 105: Virtual File System Implementation
For example, Linux has four object types:
  inode, file, superblock, dentry
VFS defines set of operations on the objects that must be implemented
  Every object has a pointer to a function table
    Function table has addresses of routines to implement that function on that object
    For example:
    • int open(. . .)—Open a file
    • int close(. . .)—Close an already-open file
    • ssize t read(. . .)—Read from a file
    • ssize t write(. . .)—Write to a file
    • int mmap(. . .)—Memory-map a file

## Slide 106: Remote File Systems
Sharing of files across a network
First method involved manually sharing each file – programs like ftp
Second method uses a distributed file system (DFS)
  Remote directories visible from local machine
Third method – World Wide Web
  A bit of a revision to first method
  Use browser to locate file/files and download /upload
  Anonymous access doesn’t require authentication

## Slide 107: Client-Server Model
Sharing between a server (providing access to a file system via a network protocol) and a client (using the protocol to access the remote file system)
Identifying each other via network ID can be spoofed, encryption can be performance expensive
NFS an example
  User auth info on clients and servers must match (UserIDs for example)
  Remote file system mounted, file operations sent on behalf of user across network to server
  Server checks permissions, file handle returned
  Handle used for reads and writes until file closed

## Slide 108: Distributed Information Systems
Aka distributed naming services, provide unified access to info needed for remote computing
Domain name system (DNS) provides host-name-to-network-address translations for the Internet
Others like network information service (NIS) provide user-name, password, userID, group information
Microsoft’s common Internet file system (CIFS) network info used with user auth to create network logins that server uses to allow to deny access
  Active directory distributed naming service
  Kerberos-derived network authentication protocol
Industry moving toward lightweight directory-access protocol (LDAP) as secure distributed naming mechanism

## Slide 109: Consistency Semantics
Important criteria for evaluating file sharing-file systems
Specify how multiple users are to access shared file simultaneously
  When modifications of data will be observed by other users
  Directly related to process synchronization algorithms, but atomicity across a network has high overhead (see Andrew File System)
The series of accesses between file open and closed called file session
UNIX semantics
  Writes to open file immediately visible to others with file open
  One mode of sharing allows users to share pointer to current I/O location in file
  Single physical image, accessed exclusively, contention causes process delays
Session semantics (Andrew file system (OpenAFS))
  Writes to open file not visible during session, only at close
  Can be several copies, each changed independently

## Slide 110: The Sun Network File System (NFS)
An implementation and a specification of a software system for accessing remote files across LANs (or WANs)
The implementation originally part of SunOS operating system, now industry standard / very common
Can use unreliable datagram protocol (UDP/IP) or TCP/IP, over Ethernet or other network

## Slide 111: NFS (Cont.)
Interconnected workstations viewed as a set of independent machines with independent file systems, which allows sharing among these file systems in a transparent manner
  A remote directory is mounted over a local file system directory
    The mounted directory looks like an integral subtree of the local file system, replacing the subtree descending from the local directory
  Specification of the remote directory for the mount operation is nontransparent; the host name of the remote directory has to be provided
    Files in the remote directory can then be accessed in a transparent manner
  Subject to access-rights accreditation, potentially any file system (or directory within a file system), can be mounted remotely on top of any local directory

## Slide 112: NFS (Cont.)
NFS is designed to operate in a heterogeneous environment of different machines, operating systems, and network architectures; the NFS specifications independent of these media
This independence is achieved through the use of RPC primitives built on top of an External Data Representation (XDR) protocol used between two implementation-independent interfaces
The NFS specification distinguishes between the services provided by a mount mechanism and the actual remote-file-access services

## Slide 113: Three Independent File Systems

## Slide 114: Mounting in NFS
Mounts
Cascading mounts

## Slide 115: NFS Mount Protocol
Establishes initial logical connection between server and client
Mount operation includes name of remote directory to be mounted and name of server machine storing it
  Mount request is mapped to corresponding RPC and forwarded to mount server running on server machine
  Export list – specifies local file systems that server exports for mounting, along with names of machines that are permitted to mount them
Following a mount request that conforms to its export list, the server returns a file handle—a key for further accesses
File handle – a file-system identifier, and an inode number to identify the mounted directory within the exported file system
The mount operation changes only the user’s view and does not affect the server side

## Slide 116: NFS Protocol
Provides a set of remote procedure calls for remote file operations. The procedures support the following operations:
  searching for a file within a directory
  reading a set of directory entries
  manipulating links and directories
  accessing file attributes
  reading and writing files
NFS servers are stateless; each request has to provide a full set of arguments (NFS V4 is newer, less used – very different, stateful)
Modified data must be committed to the server’s disk before results are returned to the client (lose advantages of caching)
The NFS protocol does not provide concurrency-control mechanisms

## Slide 117: Three Major Layers of NFS Architecture
UNIX file-system interface (based on the open, read, write, and close calls, and file descriptors)
Virtual File System (VFS) layer – distinguishes local files from remote ones, and local files are further distinguished according to their file-system types
  The VFS activates file-system-specific operations to handle local requests according to their file-system types
  Calls the NFS protocol procedures for remote requests
NFS service layer – bottom layer of the architecture
  Implements the NFS protocol

## Slide 118: Schematic View of NFS Architecture

## Slide 119: NFS Path-Name Translation
Performed by breaking the path into component names and performing a separate NFS lookup call for every pair of component name and directory vnode
To make lookup faster, a directory name lookup cache on the client’s side holds the vnodes for remote directory names

## Slide 120: NFS Remote Operations
Nearly one-to-one correspondence between regular UNIX system calls and the NFS protocol RPCs (except opening and closing files)
NFS adheres to the remote-service paradigm, but employs buffering and caching techniques for the sake of performance
File-blocks cache – when a file is opened, the kernel checks with the remote server whether to fetch or revalidate the cached attributes
  Cached file blocks are used only if the corresponding cached attributes are up to date
File-attribute cache – the attribute cache is updated whenever new attributes arrive from the server
Clients do not free delayed-write blocks until the server confirms that the data have been written to disk

## Slide 121: End of Chapter 15